ENGINEERING SPECIFICATIONS

TRS 370 Full-Height Turnstile – Single Passageway

# SECTION 11 14 00– Pedestrian Access Control Equipment (Gates/Turnstiles)

## PART I – GENERAL

  - SECTION INCLUDES

This section covers the furnishing and installation of a Full-Height Turnstile for pedestrian access control.

  - RELATED SECTIONS

** NOTE TO SPECIFIER ** Add required sections to this project

  - REFERENCES

** NOTE TO SPECIFIER ** Compliance with EC norms is the standard for the full-height turnstile. For an additional cost, compliance with UL 325 standards is available as an option listed in brackets.

Select from the following subparagraphs.

        - The full-height turnstile shall be compliant with EC standards.

        - [The full-height turnstile shall be UL 325 certified]

  - SYSTEM REQUIREMENTS

        - The pedestrian full-height turnstile shall control and be able to restrict pedestrian traffic between public and secure areas

Shall feature normally closed full-height rotating obstacle to securely block the pedestrian’s path and prevent access in restricted areas without authorisation

Shall be manually operated and bidirectional, allowing traffic in both directions. Each direction shall be independently configurable in one of three states:

Free: all persons are authorised to pass under all conditions

Controlled: each person must present a valid means of authentication to the reader before being authorised to pass

Locked: no persons are authorised to pass, and authentication means are ignored

Shall use the building access control system to grant or deny access to the facility and operate with a variety of user authentication devices

Shall be designed to guarantee user safety and ease of passage

Design of the unit shall provide visual notifications for intuitive process and high throughput

Shall be suitable for outdoor installations

  - SUBMITTALS

        - Submit product data: equipment description, dimensions, electrical wiring diagrams for installation, and manufacturer's technical manuals on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Operation and maintenance manuals.

Provide shop drawings and indicate component connections and location, anchorage methods and location, and installation details.

  - DELIVERY, STORAGE AND HANDLING

        - Deliver equipment to job site in manufacturer’s packaging, undamaged and complete with installation instructions.

Store off of the ground, under cover, protected from weather, construction activities and debris.

  - PROJECT/SITE CONDITIONS

        - Install full-height turnstile on a level finished floor.

  - QUALITY ASSURANCE

        - All components and sub-assemblies shall be manufactured in the European Union

Manufacturer Qualifications:

Manufacturer shall be a company specialising in designing and manufacturing full-height turnstiles with a proven minimum experience of fifteen (15) years

Manufacturer with well-proven experience in public transport is recommended

Manufacturer shall have a Quality Management System compliant with ISO 9001:2000.

Source Limitations: obtain Full-Height Turnstiles through one source from Automatic Systems.

###### WARRANTY

        - Automatic Systems warranties its products against defects in material and workmanship for a period of five (5) years from the date of invoicing for installations in an urban or rural environment. This warranty excludes normal wear on finishes or damage that occurs due to abuse or misuse. Obtain full warranty terms from Automatic Systems.

        - Automatic Systems warranties its products against defects in material and workmanship for a period of three (3) years from the date of invoicing for installations in an aggressive industrial or marine environment (less than ten (10) kilometers (6 1/5 miles) from the coast). This warranty excludes normal wear on finishes or damage that occurs due to abuse or misuse. Obtain full warranty terms from Automatic Systems.

## PART II – PRODUCTS

  - MANUFACTURERS

        - Manufacturers: subject to compliance with requirements, provide products by one of the following:

AUTOMATIC SYSTEMS, 5 Avenue Mercator, 1300 Wavre, BELGIUM

Phone : +32-(0)10 230 211   Fax : +32-(0)10 230 202

Homepage : www.automatic-systems.com   E-mail : asmail@automatic-systems.com

Products:

Full-Height Turnstile, Model TRS 370

  - CONSTRUCTION

** NOTE TO SPECIFIER ** RAL 7038 painted galvanized steel is the standard finish for the frame and the mechanism housing. For an additional cost, customised RAL paint is available as an option listed in brackets to perfectly suit all architectural surroundings.

Delete the following subparagraphs in brackets if no optional finish is required, or retain as necessary and specify the required RAL paint for this project.

        - Frame

To be manufactured from galvanized steel structure with two (2) coats of pale grey paint RAL 7038

[To be manufactured from galvanized steel structure with two (2) coats of paint RAL xxxx (to be specified)]

Mechanism housing

To be manufactured from steel treated by electrophoresis with 2 coats of pale grey paint RAL 7038

[To be manufactured from steel treated by electrophoresis with 2 coats of paint RAL xxxx (to be specified)]

Shall be designed with a diamond point roof for evacuation of water

Doors shall be key-locked

Rotating obstacle

** NOTE TO SPECIFIER ** RAL 7038 painted galvanized steel is the standard finish for the rotating obstacle. For an additional cost, brushed stainless steel type AISI 304 is available as an option listed in brackets.

Delete the following subparagraph in brackets if no optional finish is required, or retain as necessary.

To be manufactured from galvanized steel structure with two (2) coats of pale grey paint RAL 7038

[To be manufactured from brushed stainless steel type AISI 304]

Enclosure

Design of the unit’s enclosure shall ensure an IP 43 degree of protection

  - DIMENSIONS

        - Lane width:

Single passageway

640 mm (25 1/5 in)

Dimensions:

Length: 1540 mm (60 5/8 in) maximum

Height: 2289,5 mm (90 1/7 in) maximum

Width: 1370 mm (54 in) maximum

  - OPERATION

        - The unit shall be manually operated in both directions

        - Normal Operation (available for “Controlled” operating mode)

In stand-by position, the passageway shall be securely blocked by means of mechanically locked rotating obstacles

Upon receipt of opening pulse from the access control system the mechanism shall unlock, consequently the user can manually operate the rotor in the authorised direction

Obstacles does immediately lock after passage or after an adjustable time-out

Power Failure

** NOTE TO SPECIFIER ** Select and retain one (1) of the following two (2) subparagraphs that is appropriate to this project.

In case of emergency or power failure, the rotating obstacle is unlocked and freely rotates to allow an easier exit (Fail-Safe). After the power supply has been restored, the unit shall return to its previous operating mode.

In case of emergency or power failure, the rotating obstacle is mechanically locked (Fail-Lock). After the power supply has been restored, the unit shall return to its previous operating mode.

Emergency Operation

The unit shall have an input in order to receive the “fire alarm” signal. When the emergency signal is activated, the rotating obstacle is unlocked and freely rotates to allow easier exit.

This operating mode continues as long as the emergency signal is active. After the emergency signal has been turned off, the unit shall return in its previous operating mode.

  - SECURITY

        - Shall provide three (3) full-height rotors with straight arms welded to securely block the passageway and ensure single-user throughput

Shall have mechanical locking integrated. The rotating obstacle shall be mechanically blocked in rest position to prevent any attempted break-in (only if at least one direction of passage is controlled) and to prevent two (2) passages at one time. The mechanical locking of rotating obstacle shall withstand a 1500 Nm torque

Passage shall be electronically controlled and independently configurable in both directions:

Free access

Permanently locked

Passage subject to authorisation

The full-high turnstile shall feature an anti-pass back mechanism that prevents reverse rotation of the obstacle after a 60° rotation from the rest position to deter any unauthorised use and fraud in the opposite direction

Shall include fixed obstacles, limiting passage and preventing any fraudulent passage in the opposite direction to the authorised passage

Shall be equipped with a self-centering mechanism to insure that rotating obstacle returns to the reset position after passage

** NOTE TO SPECIFIER ** For an additional cost, a canopy is available as an option listed in brackets to prevent any climbing attempts.

Retain or delete the following subparagraph according to the project requirements.

[Shall be equipped with a canopy to improve weather protection and securely block any climbing attempts]

  - SAFETY AND ERGONOMICS

        - Shall have three (3) rotors spaced at 120° to allow comfort and ease of passage

Shall be cushioned by a hydraulic shock absorber to ensure a smooth, silent and progressive movement

** NOTE TO SPECIFIER ** For an additional cost, a selection of options is available listed in bracket to enhance ease of passage and user safety.

Select and retain the one (1) or two (2) following subparagraph(s) that is (are) appropriate for this project.

[Shall be equipped with heel protectors that cushion the lowest arms of the rotating obstacle for additional user protection]

[Shall provide manual release kit to mechanically unlock the rotating obstacle, regardless of the chosen operating mode]

  - PEDESTRIAN GUIDANCE

        - Visual notification with clear graphics shall be incorporated into each passageway (one for each direction) to provide status of the lane, to control flow and to warn users

Passageway shall be illuminated by LED integrated lighting to improve user comfort and safety

  - CONTROLLER

        - Microprocessor-based controller with the following characteristics:

RAM & ROM memory

CAN Bus interface

LCD display to set operating modes, advanced parameters and to provide diagnostics for quick detection of problem source

LED indicators showing the status of the inputs and outputs

RS232 communication interface for extended settings and functions

  - POWER SUPPLY

Power supply:

** NOTE TO SPECIFIER ** Retain one (1) of the following two (2) subparagraphs to select power supply

230 Volts AC 50/60 Hz

120 Volts AC 60 Hz

Nominal consumption in operation: 70 W maximum

  - PERFORMANCES

        - MCBF: 1.000.000 average number of cycles between breakdowns, when respecting recommended maintenance

Operating Temperatures: -10 to +50 degrees Centigrade (+14 to +122 degrees Fahrenheit)

  - OPTIONAL EQUIPMENT

** NOTE TO SPECIFIER ** Delete the following subparagraphs in brackets if no optional equipment is required, or add as necessary.

[Reader support for integration of user authentication devices]

[Heating resistance for operation to -35 degrees Celsius (-31 degrees Fahrenheit)]

[Foundation fixing frame]

## PART III – EXECUTION

  - INSPECTION

        - Installer must examine the installation location and advise the Contractor of any site conditions inconsistent with proper installation of the product. These conditions include but are not limited to the following:

Full-height turnstile must be installed on a level concrete pad

Power supply and control wiring must be installed. Follow manufacturer’s recommendations

Proceed with installation only after unsatisfactory conditions have been corrected.

  - INSTALLATION

        - Install full-height turnstile in strict accordance with manufacturer’s instructions. Set units level. Anchor securely into place.

  - ADJUSTMENT

        - Installer shall adjust full-height turnstile for proper performance after installation.

  - INSTRUCTION

        - A factory trained installer shall demonstrate to the owner’s maintenance crew the proper operation and the necessary service requirements of the equipment, including exterior maintenance.

  - CLEANING

        - Clean turnstile and area carefully after installation to remove excess caulk, dirt and labels.

  - MAINTENANCE

        - Maintain the equipment according to the manufacturer’s instructions.

Automatic Systems reserves the right to change this specification at any time without notice.

END OF SECTION